## Slide 1: ONVIF Audit Tool
By Roger Hardiman
ONVIF Open Source Challenge

## Slide 2: ONVIF Audit Tool
The Problem
Need a list of the Make, Model, Firmware Version of all the ONVIF cameras on the network
Need a JPEG snapshot to show the image view or image quality in different light levels
Has to support
  Multiple makes of ONVIF Camera
  Mixture of different firmware versions
  Mixture of different usernames and passwords
ONVIF Audit Tool

## Slide 3: ONVIF Audit Tool
The Solution
Utility that carries out an ONVIF Audit
Produces a folder containing a log file for each camera and a JPEG for each camera
Folder /onvif_audit_report_2018_05_31_09_05_00
camera_report_123.157.208.28.txt snapshot_123.157.208.28.jpg
camera_report_193.159.244.132.txt snapshot_193.159.244.132.jpg
camera_report_193.159.244.134.txt snapshot_193.159.244.134.jpg
camera_report_60.191.94.122.txt snapshot_60.191.94.122.jpg
camera_report_61.164.52.166.txt snapshot_61.164.52.166.jpg
ONVIF Audit Tool

## Slide 4: ONVIF Audit Tool
Using a
Config File
Use a config file with a list of IP addresses, usernames and passwords using a file in the industry standard JSON format
>onvif-audit --filename camera_list.json
Contents of camera_list.json :-
"cameralist": [
{
"ipaddress": "193.159.244.132-193.159.244.134",
"port": "80",
"username": "service",
"password": ”the password",
"comment": "Bosch"
}
] }

## Slide 5: ONVIF Audit Tool
Using the
Command Line
Use the command line with an IP address (or a range of IP addresses) and the username and password
>onvif-audit –ipaddress 192.168.1.1 –username user –password passwd
>onvif-audit –ipaddress 192.168.1.1-192.168.1.20 –username user –password passwd

## Slide 6: ONVIF Audit Tool
Outputs
JPEG Snapshot for each camera
Log file for each camera. An example is
Host:= 60.191.94.122 Port:= 8086
Date:= Thu May 31 2018 06:39:49 GMT+0100 (BST)
Manufacturer:= Dahua
Model:= IPC-HDW4830EM-AS
Firmware Version:= 2.622.0000000.21.R, Build Date 2018-02-03
Serial Number:= 2E05F8AYAW00038
Hardware ID:= 1

## Slide 8: ONVIF Audit Tool
By Roger Hardiman
ONVIF Open Source Challenge

## Slide 9: ONVIF Audit Tool
The Problem
Need a list of the Make, Model, Firmware Version of all the ONVIF cameras on the network
Need a JPEG snapshot to show the image view or image quality in different light levels
Has to support
  Multiple makes of ONVIF Camera
  Mixture of different firmware versions
  Mixture of different usernames and passwords
ONVIF Audit Tool

## Slide 10: ONVIF Audit Tool
The Solution
Utility that carries out an ONVIF Audit
Produces a folder containing a log file for each camera and a JPEG for each camera
Folder /onvif_audit_report_2018_05_31_09_05_00
camera_report_123.157.208.28.txt snapshot_123.157.208.28.jpg
camera_report_193.159.244.132.txt snapshot_193.159.244.132.jpg
camera_report_193.159.244.134.txt snapshot_193.159.244.134.jpg
camera_report_60.191.94.122.txt snapshot_60.191.94.122.jpg
camera_report_61.164.52.166.txt snapshot_61.164.52.166.jpg
ONVIF Audit Tool

## Slide 11: ONVIF Audit Tool
Using a
Config File
Use a config file with a list of IP addresses, usernames and passwords using a file in the industry standard JSON format
>onvif-audit --filename camera_list.json
Contents of camera_list.json :-
"cameralist": [
{
"ipaddress": "193.159.244.132-193.159.244.134",
"port": "80",
"username": "service",
"password": ”the password",
"comment": "Bosch"
}
] }

## Slide 12: ONVIF Audit Tool
Using the
Command Line
Use the command line with an IP address (or a range of IP addresses) and the username and password
>onvif-audit –ipaddress 192.168.1.1 –username user –password passwd
>onvif-audit –ipaddress 192.168.1.1-192.168.1.20 –username user –password passwd

## Slide 13: ONVIF Audit Tool
Outputs
JPEG Snapshot for each camera
Log file for each camera. An example is
Host:= 60.191.94.122 Port:= 8086
Date:= Thu May 31 2018 06:39:49 GMT+0100 (BST)
Manufacturer:= Dahua
Model:= IPC-HDW4830EM-AS
Firmware Version:= 2.622.0000000.21.R, Build Date 2018-02-03
Serial Number:= 2E05F8AYAW00038
Hardware ID:= 1

## Slide 14: ONVIF Audit Tool
Future
RoadMap
Use the PTZ Absolute Position to capture JPEGs from different directions on Pan/Tilt/Zoom cameras
Graphical User Interface to allow novice users to enter IP address range, username and password